## Slide 1: Doodle Drive
Team 6
Alexander Curtis
Peachanok Lertkajornkitti
|
Jun Pan
|
Edward Kidarsa
|

## Slide 2: Outline
Project overview
Project-specific success criteria
Block diagram
Component selection rationale
Packaging design
Schematic and theory of operation
PCB layout
Software design/development status
Project completion timeline
Questions / discussion

## Slide 3: Project Overview
Android application as controller
Robot vehicle with microcontroller
Path will be drawn in Android application and the vehicle will follow that path
  Outdoor mode with GPS, Google Maps, Compass
  Indoor mode with tilt control

## Slide 4: Project-specific success criteria
1. An ability to send and receive encoded data to an Android Device via Bluetooth
2. An ability to make a turn without stopping
3. An ability to navigate to a designated GPS coordinate with some approximation (GPS uncertainty of about ~5m)
4. An ability to monitor the battery power level
5.An ability to detect obstacles 0.5m away in a ~120 degree field of vision and alert user (vibrate)

## Slide 5: Block Diagram
PWM

## Slide 6: Component selection rationale
MICROCONTROLLER
BLUETOOTH
POSITIONING:
  GPS
  COMPASS
POWER:
  FUEL GAUGE
  BATTERY RE-CHARGE CHIP

## Slide 7: MICROCONTROLLER RATIONALE
NXP LPC1768
  mBed prototyping environment and compiler
    Quick and efficient prototyping with mbed SDK
    Ease of use
    Good amount of sample code/libraries exist
  Enough ports for necessary peripherals
    3x UART, 2x I2C, 6x PWM channels
    Input capture pins with timer
Notes: Quick prototyping with mbed SDK
Easy to move from module to custom PCB

## Slide 8: POSITIONING/Communication Components RATIONALE
GPS: UP-501
  Most cost effective according to comparison study (Sparkfun)
  Low power consumption ~80mW
  Configurable update rate (up to 10 Hz)
  High accuracy ~2.5m
BLUETOOTH: RN-41
  Class 1 device (range up to 100m as opposed to Class 2, 10m)
  LEDs indicating the status of the connection
Compass: LSM303DLM
  Cheapest 3-axis compass with tilt compensation

## Slide 9: POWER components RATIONALE
FUEL GAUGE: LTC4150
  Compatible with six NiMH cell configuration
  Low feature and simple interfacing
    Interrupt counting or input capture
BATTERY RE-CHARGE CHIP:
  Compatible with six NiMH cell configuration
  Switch mode charging for high efficiency and low heat dissipation
  Accurate charge termination (dT/dt method) for safety

## Slide 10: PACKAGING DESIGN
Durable rugged body and wheels
Large enough to fit components on the PCB
Mounted PCB
Portable
Minimal mechanical components

## Slide 11: PACKAGING DESIGN

## Slide 12
Notes: Here’s an overview of our schematic – it’s essentially split into components that have to do with actual operation (bottom left) and power components (top right). I’ll be covering the microcontroller first and then the logic components surrounding it and then finish off with the power components

## Slide 13: MicroController
1: Compass (I2C)
2: Bluetooth (UART)
3: GPS (UART)
4: H-Bridge (PWM, GPIO)
5: Ultrasonic (GPIO)
6: Optical Encoders (Input Capture, GPIO)
7: Crystal Oscillator
8: Fuel Gauge (GPIO)
9: Servo (PWM)
1
3
7
8
2
4
9
5
6
Notes: Limited # of UART ports – 4 Total, 1 is used for Mbed testing, 1 overlaps with I2C, and that leaves 2 leftover – one for GPS, one for Compass
Only 2 I2C ports total, which is plenty, but they are right next to eachother. Bluetooth modules mainly only work with I2C
Spaced things out as best as possible.
Input capture for

## Slide 14: COMPASS
Notes: Here’s the compass – the symbol looks a little odd but it’s this way because we’re actually using a breakout board for it (you can see this better on the PCB) because the IC itself is incredibly small. The breakout board has a bypass capacitors on it already. All that’s connected is the two pullup I2C resistors. There are a lot of unused pins, mainly because this device is more feature heavy than we need and actually has an accelerometer too.

## Slide 15: GPS

## Slide 16: BLUETOOTH

## Slide 17: Ultrasonic / Encoder / Servo

## Slide 18: H-BridgE
Notes: Hbridge. We currently have two 100nF capacitors for bypass (as specified by datasheet). For each motor, it takes in one gpio (enable) and two pwm channels (for controlling operation). We could connect sense resistors at SENSE_A and SENSE_B and have a pin monitoring the voltage at those so we know the current they’re using, but we aren’t doing that right now. You can see to the left two headers for each motor, as well as four flyback diodes that are used for protection (not internal to L298)

## Slide 19: Reset / ProgramminG Switch
Notes: This is the bottom left. The first thing to note is the programming header. This actually interfaces with the mBed prototype board which converts this serial to USB so it can interact with a computer. ISPSEL is used to put it into programming mode. Pin 6 on this header you’ll see is connected to a switch. When this switch is in the upward position (as it is is shown) it is connected to the microcontroller reset pin. This allows our application to automatically put the micro into reset mode once we have the pins connected to the header. On the other hand, when the program switch is down, it is just connected to a push button so we can reset the micro.

## Slide 20: FUEL GAUGE
Notes: This is our fuel gauge. This is actually a bit different than the schematic you have. The two resistors are pull up resistors for !INT and POL since they are both open drain outputs. INT will assert low whenever it detects a unit of charge so the microcontroller will be keeping track of this. Simultaneously, POL will be read – showing the polarity of the charge (charging or discharging). The sense resistor was chosen to not have a voltage drop exceeding 50mV and we will at most have 25mV drop. Finally, the C22 filter capacitor averages noise

## Slide 21: VOLTAGE REGULATORS
Notes: As you’ve seen a lot of components that use 3.3V and then a few that use 5V, we have two step down regulators – they are switch mode for higher efficiency since we’re running off battery - these are pretty standard circuits and the data sheet was followed. The input capacitor is low ESR, and the output capacitor is electrolytic. We used TI’s bench simulation software to pick ideal values.

## Slide 22: RECHARGE CIRCUIT
Notes: Finally, this is the recharge circuit. The IC at the middle of this is the Maxim DS2715. This facilitates charging of the battery pack and is set up to run in switched mode. It has various modes – precharge, fast charge, top off, etc. – that are controlled and entered based on various conditions. The most important is fast charge, which has a charging current of ~1A set by the sense resistor. This mode is terminated by the thermal resistor (THERM1) placed physically next to the battery pack. It will sense the temperature and, when the battery is done charging and converted excess energy into heat, will discontinue the charging. The LED displays the mode of charging. There is also a backup termination mode based on timeout (this is set by the resistor on RT) and ours is currently set to ~160 minutes The Vch pin essentially toggles on and off depending on the sense resistor which will effect the operation of the mosfets – a lot of that circuit is used to improve switching times whereas the power MOSFET Q3 is the main control (Vch controls switching operation).

## Slide 23: PCB LAYOUT: DESIGN CONSIDERATIONS
GPS far away from everything
  Especially active circuits such as regulators
Bluetooth away from power supply
  No traces / ground plane / vias allowed under antenna
  Antenna end protrude 5mm beyond any enclosure
Traces
  0.016 in used for most traces
  Power and Ground traces used 0.040 when possible, some pins were too small
Routing
  45 degrees routings were used as much as possible
  T intersections were used to avoid acute angles

## Slide 24: PCB LAYOUT – 7.3 x 5.5 in

## Slide 26: PCB LAYOUT: Micro
Center of PCB to be accessible to everything else
Headers on all sides for access to pins ( debugging etc )
Bypass capacitors placed next to micro before headers
External oscillator used
  Located near the microcontroller after header
Routing
  GPS and H-Bridge was on either ends of the board, thus had long connecting traces
Traces
  Due to the small size of the pins, only 0.01 in traces were able to be used
JTAG header is connected to Micro

## Slide 27: PCB LAYOUT: Micro

## Slide 28: PCB LAYOUT: Micro

## Slide 29: PCB LAYOUT: POwer
Power Circuit:
  2 Motors, H-Bridge, Battery Recharge Circuit, 2 Voltage Regulators
  Power circuit located near edge of PCB away from transmission peripherals
  Placed near each other
  Power circuits may have current feedback / current spikes need wider traces than the rest of the circuit

## Slide 30: PCB LAYOUT: VOLTAGE REGULATORS
+ FUEL GAUGE
Notes: the PC board copper area connected to this pin should be kept to a minimum.
Open core inductors may cause interference / noise / stray inductance
Large Copper Area / airflow might be needed if current load > 2A

## Slide 31: PCB LAYOUT: VOLTAGE REGULATORS
+ FUEL GAUGE
Notes: the PC board copper area connected to this pin should be kept to a minimum.
Open core inductors may cause interference / noise / stray inductance
Large Copper Area / airflow might be needed if current load > 2A

## Slide 32: PCB LAYOUT: CHARGING CHIP
PIN HEADER TO BATTERY

## Slide 33: PCB LAYOUT: CHARGING CHIP
PIN HEADER TO BATTERY

## Slide 34: PCB LAYOUT: MOTORS
Notes: Limited # of UART ports – 4 Total, 1 is used for Mbed testing, 1 overlaps with I2C, and that leaves 2 leftover – one for GPS, one for Compass
Only 2 I2C ports total, which is plenty, but they are right next to eachother. Bluetooth modules mainly only work with I2C
Spaced things out as best as possible.
Input capture for

## Slide 35: PCB LAYOUT: MOTORS
Notes: Limited # of UART ports – 4 Total, 1 is used for Mbed testing, 1 overlaps with I2C, and that leaves 2 leftover – one for GPS, one for Compass
Only 2 I2C ports total, which is plenty, but they are right next to eachother. Bluetooth modules mainly only work with I2C
Spaced things out as best as possible.
Input capture for

## Slide 36: PCB LAYOUT: PERIPHERALS

## Slide 37: PCB LAYOUT: GPS + BLUETOOTH
Notes: Limited # of UART ports – 4 Total, 1 is used for Mbed testing, 1 overlaps with I2C, and that leaves 2 leftover – one for GPS, one for Compass
Only 2 I2C ports total, which is plenty, but they are right next to eachother. Bluetooth modules mainly only work with I2C
Spaced things out as best as possible.
Input capture for

## Slide 38: PCB LAYOUT: GPS + BLUETOOTH
Notes: Limited # of UART ports – 4 Total, 1 is used for Mbed testing, 1 overlaps with I2C, and that leaves 2 leftover – one for GPS, one for Compass
Only 2 I2C ports total, which is plenty, but they are right next to eachother. Bluetooth modules mainly only work with I2C
Spaced things out as best as possible.
Input capture for

## Slide 39: PCB LAYOUT: Compass + Servo + JTAG +
JTAG PROGRAMMING PINS
ULTRASONIC SENSOR+ OPTICAL ENCODER + OSCILLATOR
Notes: Limited # of UART ports – 4 Total, 1 is used for Mbed testing, 1 overlaps with I2C, and that leaves 2 leftover – one for GPS, one for Compass
Only 2 I2C ports total, which is plenty, but they are right next to eachother. Bluetooth modules mainly only work with I2C
Spaced things out as best as possible.
Input capture for

## Slide 40: PCB LAYOUT: Compass + Servo + JTAG +
JTAG PROGRAMMING PINS
ULTRASONIC SENSOR+ OPTICAL ENCODER + OSCILLATOR
Notes: Limited # of UART ports – 4 Total, 1 is used for Mbed testing, 1 overlaps with I2C, and that leaves 2 leftover – one for GPS, one for Compass
Only 2 I2C ports total, which is plenty, but they are right next to eachother. Bluetooth modules mainly only work with I2C
Spaced things out as best as possible.
Input capture for

## Slide 41: Software Preliminary Design
Microcontroller
  Done testing:
    Ultrasonic sensors, H Bridge, Servo, Bluetooth
  Need to test:
    Compass (I2C)
    GPS (UART)
    Fuel Gauge (I/O)

## Slide 42: Software Preliminary Design
Notes: Basic state diagram of our software design
Timer interrupt to report status of the GPS location, heading, battery statu, etc periodically.

## Slide 43: Software Preliminary Design
Android application
  Google Maps API
  Battery status bar
  Toggle switch between Indoor/Outdoor modes
  Progress:
    Android output angles when tilting (for Indoor Mode)
    Google Maps displays on screen with ability to draw lines/polygons on screen
    Battery status bar
    Bluetooth interface

## Slide 44: PROJECT TIMELINE
Week | Test all components | Finalize PCB | Test and Debug Micro code | Test & Debug Android code | Test each parts on PCB | Finish packaging | PSSC & Final Presentation
8 |  |  |  |  |  |  | 
9 |  |  |  |  |  |  | 
10 |  |  |  |  |  |  | 
11 |  |  |  |  |  |  | 
12 |  |  |  |  |  |  | 
13 |  |  |  |  |  |  | 
14 |  |  |  |  |  |  | 
15 |  |  |  |  |  |  | 
16 |  |  |  |  |  |  | 

## Slide 45
THANK YOU!
Questions / Discussions